Анотація. У роботі виконано тепловий та гідравлічний розрахунок кінцевого охолоджувача повітря турбокомпресора ТК-250-61-5. У результаті теплового розрахунку визначені значення термодинамічних та конструктивних параметрів апарату, що проектується. У результаті гідравлічного розрахунку визначено гідравлічний опір апарату. Також було виконано розрахунки на міцність елементів охолоджувача повітря, таких як циліндрична обичайка та пласке днище і розрахунок на міцність та герметичність фланцевого з’єднання.

Ключові слова: кінцевий охолоджувач повітря, турбокомпресор, тепловий розрахунок, гідравлічний розрахунок, розрахунок на міцність.

Abstract. A thermal and hydraulic calculation of the terminal air cooler of the TC-250-61-5 turbocharger was performed. As a result of the thermal calculation, the values of the thermodynamic and design parameters of the projected apparatus are determined. As a result of the hydraulic calculation, the hydraulic resistance of the apparatus was determined. Calculations were also made on the strength of air cooler elements, such as a cylindrical shell and a flat bottom, and a calculation on the strength and tightness of a flange joint.

Keywords: terminal air cooler, turbocharger, heat calculation, hydraulic calculation, strength calculation.